## Slide 1: Compressed Sensing MRI
Drew McCallister

## Slide 2: How MRI works
Gradient Fields applied in X , Y and Z directions
  Ex: B= B0+Gx
2-D acquisitions:
  Slice selection gradient (Z)
  Phase(X) and Freq.(Y) gradient move through 2-D k-space
  NxN k-space matrix Fourier transformed to NxN image
Illustration of z-gradient
Spins are in external magnetic field B0
R-F pulse flips spins which precess at =B
B0
R-F

## Slide 3: The Problem
Larger Gradients -> Higher Freq. in K-space -> Higher Resolution
  Theoretically MRI resolution is dependent on Gradient Strength
In practice we image living things
->Practically, scan time limits resolution
Fourier Transform

## Slide 4: How do we reduce K-space points but not resolution?
What prior knowledge do we have about MRI k-space?
Symmetrical
  Partial Fourier reconstruction
  Projection Onto Convex Sets (POCS)
Compressible
  Under wavelet or other transform, MRI images are sparse
Discrete Wavelet Transform
It would be great if we could acquire in DWT space and only acquire the interesting points
……. But we can’t
Histogram of Pixel Magnitude
Significant
Insignificant

## Slide 5: Compressed Sensing
=
Y
X
Φ
If we know X is sparse,
can we invert Φ to get X from Y?
Theorem: If Φ satisfies Restricted Isometry Property (RIP), then x is unique, sparse solution to Φx=y
Meaning: If Φ is nearly an orthogonal matrix,
we can recover x by solving:
min|x|0 such that Φx=y
Lp norms: |x|p=(Ʃ|x|p)1/p where |x|0 is the number of non-zero entries

## Slide 6: Application to MRI
Minimizing the L0 norm is computationally very expensive
L1 norm is convex and much simpler to minimize
->Theorem: L1 min = L0 min if Φ satisfies RIP to a more stringent limit
Applying to MRI:
Fourier transforming k-space “f” to get image “u” that we sparsify with wavelet transform “W” and minimize
min|Wu|0= such that Fu=f
In practice due to noise we don’t enforce Fu=f
min|Wu|0= such that |Fu-f|2<σ

## Slide 7: Minimization
If we randomly under sample our k-space, satisfies RIP
Split-Bregman Method
  Modified Bregman-Iteration method
    commonly used for L1 minimization
Used Haar wavelet for DWT
Compressed Sensing Test Sparsity = 25%
Original Image
Under-sampled k-space
Recovered Image
Under-sampled image

## Slide 8: Brain image with Sparsity = 50%
Original Image
Under-sampled k-space
Under-sampled Image
Recovered Image

## Slide 9: Future Directions
Minimization performance depends on a length-scale gamma
  -Characterize parameter space for relevant image types
Implement compressed sensing for 3-D k-space images

## Slide 10: Compressed Sensing
Allows for recovery of data that is sparse in a wavelet basis from a randomly under-sampled “sensing” measurement basis
Applications far beyond MRI
  Sensor Networks and data acquisition
    Reduction of power consumption and reduced sensor processing
  Astronomy
    Reconstruction of signal from incomplete and noisy data
  Linear coding
    Reconstruction of corrupted transmissions
Good short intro for those interested:
Terrence Tao’s blog on single pixel cameras